# Tips for assembling the PT platform with servos

-please refer to the photos in our ebay listing for how the PT platform parts fit together.

-always make sure each servo is free to move in the range you wish.  Some adjustment may be needed before screwing in all screws.

-the MG90 servo is a tight fit when assembling the base, but the 2 base parts will go together with some pressure.  If needing to separate the 2 parts of the base, prise apart with a flathead screwdriver.

-all servo horns will need trimming to fit.  In the base it is not necessary to embed the horn (recommend the cross 4way horn), as the screws will reach through from the bottom of the base.

-it is recommended to use the screws supplied with the PT platform generally, except for fixing the servo horns to the servos.  In that case use the screws supplied with the servos.

-the longer length bolts and nuts are for affixing the second, vertical axis servo. Adjust the tightness of the fixing until there is easy movement in the vertical pivot, then affix the servo horn.   Glue and/or threadlock can be used if desired.

-attaching the camera will depend on your camera.  A camera with case should slot straight into the clips, but a board camera will need some trimming of the clips depending on the model or some extra fixing such as glue or tape.