DC12V 1CH Receiver Board

1.Working Voltage: DC12V±10%
2.Current：Standby≤10mA，Working ≤128mA
3.Working Temperature： -10℃—+60℃
4.Receiver Frequency： 315MHz/433MHZ
5.Receiving Sensitivity： -105dB
6.Output State： Switching Value
7.Max Load：10A Relay, Resistive load≤8A，Inductive load≤3A
8.Receiver Board Size：55×31×16mm
9.Case Size：73×36×24mm

Learning Code: Add transmitter by the Learning Button on the receiver

Output State:     It is adjusted by the Jumper on the Receiver Board, (before you change it .you need turn OFF the power. Until you have changed it, then turn ON the power again, or the State will not be changed)

Momentary----------Jumper on “1&2”

Toggle----------------Jumper “2&3”

Latched--------------Take away the Jumper or put the Jumper on 1 Pin

Momentary------------Press the Transmitter button and keep, the receiver relay is ON, release button, the receiver relay is OFF,

Toggle---------------Press transmitter button for 1 time, the receiver relay is ON, press button again, the receiver relay is OFF,

Latched------------------Press transmitter button A, the receiver relay A is ON, Press Button B, the Receiver is OFF

Learning Method:
Input power for the Receiver .Press the Learning Button until the Led indicator ON. Then press transmitter, the Led indicator flash fast, it mean learning successfully.
Clearing Code
Keeping press the Learning Button on the receiver until the LED indicator ON and flash fast, it mean the code have been cleared successfully.

FAQs
Q Why is there no voltage output from the switch?  
A There is no voltage output, the switch acts as a connecter or disconnecter for an existing live circuit.

Q Why is there no response from the switch when the remote is pressed?
A First try clearing the remote by holding down the learning button until the led light flashes, then add the remote again.  If this doesn't work try changing the battery in the remote.

Q How do I extend the range?
A This is possible by ensuring there are no obstacles, the remote has a good battery and the receiver a good power supply.  Also the receiver aerial can be gently extended.