DC12V 2CH Receiver Board

Working Voltage: DC12V

Output Current: 10A

Channel: 2CH

Working Frequency: 315/433MZH

Receiver sensitivity: -105Db

Working temperature: -10'C - +60'C

Encoding Type: Learning Code (add transmitter by the learning button on the receiver)

Output State: It is adjusted by the Jumper on the Receiver Board, (before you change it .you need turn OFF the power. Until you have changed it, then turn ON the power again, or the State will not be changed)

Momentary------------Press the Transmitter button A, the receiver relay A is ON, release button A; the receiver relay A is OFF, the same as B Button and Relay B. 2CH are independent .

Toggle---------------Press transmitter button A for 1 time, the receiver relay A is ON, press button A again, the receiver relay A is OFF, the same as B Button and B Relay. 2CH are independent

Latched------------------

Press transmitter button A, the receiver relay A is ON, the relay B is OFF.

Press transmitter button B, the receiver relay B is ON, the relay A is OFF.

It also mean .Latched only can keep 1CH ON .and it will often have 1CH is ON.

Clearing Method:

Keeping press the Learning Button on the Receiver, the LED indicator flash fast and then release, , it mean clear successfully.

Learning Method:

Press the Learning Button, the LED indicator ON  ,then press the transmitter Button A, the LED indicator flash fast and then press the Transmitter Button B right now, the LED indicator flash fast again, It means learning successfully.

FAQs
Q Why is there no voltage output from the switch?  
A There is no voltage output, the switch acts as a connecter or disconnecter for an existing live circuit.

Q Why is there no response from the switch when the remote is pressed?
A First try clearing the remote by holding down the learning button until the led light flashes, then add the remote again.  If this doesn't work try changing the battery in the remote.

Q How do I extend the range?
A This is possible by ensuring there are no obstacles, the remote has a good battery and the receiver a good power supply.  Also the receiver aerial can be gently extended.